## Slide 1
BROUGHT TO YOU BY CANSO:
ASSESSING THE
IMPACT OF WIND FARMS
ON AERONAUTICAL RADAR SYSTEMS
Tuesday 28 April 2026
11:00 – 12:00 UTC

## Slide 4
BROUGHT TO YOU BY CANSO:
ASSESSING THE
IMPACT OF WIND FARMS
ON AERONAUTICAL RADAR SYSTEMS
Tuesday 28 April 2026
11:00 – 12:00 UTC

## Slide 5
John Wennes
Safety Programme Manager
CANSO
MODERATOR

## Slide 6
Yahya Khaled
General Manager
ATDI Limited (Middle East)
PRESENTER

## Slide 7: Impact of Wind Farms on Radars
By Yahya Khaled – GM, ATDI Limited
April 2026
A technical webinar on wind turbine interference with primary and secondary surveillance radars
www.atdi.com
Notes: This webinar aims to provide a clear, practical understanding of how the rapid expansion of wind energy can affect radar systems used in aviation. It introduces the key interference mechanisms and their operational impacts, then focuses on how these effects are assessed using established frameworks such as EUROCONTROL and NTIA methodologies. The goal is to equip participants with a structured approach to evaluating and mitigating radar impacts, enabling the safe and efficient coexistence of wind farms and air traffic surveillance.

## Slide 8
A Global Leader in Spectrum Management
Welcome to ATDI
11 boulevard Malesherbes, 75008 Paris, FRANCE
ATDI Group
www.atdi.com
contact@atdi.com
+33 1 53 30 81 41
Notes: ATDI is a global technology company specializing in radio spectrum management and wireless network engineering solutions. Founded in 1988, it develops advanced software and services that help governments, regulators, defense organizations, and network operators plan, model, and manage the use of the radio spectrum efficiently.

## Slide 9: Agenda
Introduction & context — wind energy expansion and radar impact Radar fundamentals — PSR vs SSR, bands, receiver behaviour Mechanisms of wind turbine interference — reflection, shadowing, Doppler Operational impact on air traffic surveillance Assessment approaches — screening vs detailed analysis EUROCONTROL PSR/SSR quick assessment framework NTIA TR-08-454 and the combined methodology Modelling techniques and a detailed impact study Mitigation options and key takeaways
www.atdi.com
Notes: In brief, the agenda is to look into the mechanisms of interference taking place between Radars and Wind Turbines, their impacts, their assessment methodologies and software modelling approaches and simulation outcomes.

## Slide 10: Why this matters — renewables meet airspace
Wind capacity is scaling fast — national plans target tens of GW of wind near existing radar infrastructure Turbines within radar line of sight can generate clutter, false targets, tracking instability, and coverage loss UK MoD flight trials (2005) and US DoD report (2006) first quantified the operational effects EUROCONTROL GUID-0130 (2014) and NTIA TR-08-454 (2008) are the reference assessment frameworks The engineering is well understood — structured assessment lets wind and aviation coexist safely
www.atdi.com
Notes: Whether you are a believer or not in global warming, you can still observe during the current regional conflicts that having a single source of energy is problematic to everyone. Diversifying energy sources help reduce the risk significantly.
KSA under 2030 vision, targeting 50% of the energy mix to produce electricity from sources such as (Gas, wind and solar), noting, 1 WT can generate power in the order of 2-3 MW.
Wind energy is expanding rapidly, with national strategies now targeting tens of gigawatts of new capacity, often in proximity to existing radar systems. This creates technical challenges, as turbines within a radar’s line of sight can introduce clutter, false targets, tracking instability, and even localized coverage loss. These effects were first rigorously quantified through UK Ministry of Defence flight trials in 2005 and a US Department of Defense report in 2006, establishing a foundation for understanding operational impacts. Since then, standardized assessment frameworks—such as EUROCONTROL’s GUID-0130 (2014) and the NTIA TR-08-454 (2008)—have provided structured methodologies to evaluate and mitigate interference. Today, the engineering principles are well established, and with careful, case-by-case analysis, wind development and aviation systems can coexist safely and effectively.

## Slide 11: Radar fundamentals — PSR vs SSR
Primary Surveillance Radar (PSR) — transmits RF energy and detects the reflected return from the target skin Relies on target radar cross section; vulnerable to any reflected energy from the environment Secondary Surveillance Radar (SSR) — interrogates an aircraft transponder on 1030 MHz; receives coded reply on 1090 MHz Does not rely on reflected energy — but interrogation and reply paths can still be blocked or reflected PSR and SSR are differently susceptible to wind turbine interference — the assessment must treat them separately. PSR/SSR often co-located.
www.atdi.com
Notes: Let’s briefly look at the two main types of radar used in air traffic surveillance.
Primary Surveillance Radar, or PSR, works by transmitting radio frequency energy and detecting the echoes reflected back from an aircraft. Because it relies on these reflections, it’s sensitive not just to aircraft, but to any objects in the environment that can reflect energy—such as wind turbines.
Secondary Surveillance Radar, or SSR, works differently. Instead of relying on reflections, it sends out an interrogation signal at 1030 megahertz, and the aircraft responds with a coded reply at 1090 megahertz. While SSR doesn’t depend on reflected energy, it can still be affected if the signal path between the radar and the aircraft is blocked or disturbed.
The key point is that PSR and SSR behave differently when it comes to interference. That means they need to be assessed separately, even though they are often located at the same site. When the two co-exist; normally protecting the PSR is sufficient to protect both PSR/SSR since the PSR is more stringent and more susceptible to interference.

## Slide 12: Radar bands — primary radar services (radionavigation)
Long range 23cm (L-band) radar (Good propagations, big targets)
  1215 – 1300MHz Radionavigation (Primary allocation)
  1300 – 1350MHz Aeronautical Radionavigation (Primary allocation)
Medium range 10cm (S-band) radar
  2700-2900 MHz Aeronautical Radionavigation (Primary allocation)
  2900-3100MHz Radionavigation (Primary allocation)
Short Range Precision 3cm (X-band) radar
  9000 – 9200MHz Aeronautical Radionavigation (primary allocation)
  9300 – 9500 MHz Radionavigation (Primary allocation)
Smaller wave-length means higher RCS for the same target and typically lower range.
www.atdi.com
Notes: Relationship between Frequency and propagations and RCS.
Higher freq -> Higher propagation losess -> Higher RCS as well.

## Slide 13: How wind turbines interact with radar
Reflection and I/N degradation — turbine RCS raises the local noise floor, lifting the detection threshold False target generation — direct echoes from the tower and blades, and ghost targets via multipath (main and side lobes) Shadow zone and beam blockage — two-way path attenuation creates a wedge of reduced detection behind the turbine Doppler contamination — rotating blades produce Doppler returns that slip through MTI/MTD filters as false moving targets Receiver and processing overload — strong returns or high false-plot counts can saturate the receiver or overwhelm the tracker
www.atdi.com
Shadow
False target
Reflections
Shadowing
False target
Notes: MTI (Moving Target Indication) and MTD (Moving Target Detection) are radar signal processing techniques used to filter out stationary clutter (ground, buildings) and detect moving targets

## Slide 14: Receiver behavior – AGC (saturation)
Hardware level
Adaptive gain – detect weak signal and deal with strong signals
Saturation/overload
Strong
Weak
Good
Very strong (Reflections)
Weak (Target)
Good
Weak
Wanted
Wanted + Unwanted
www.atdi.com

## Slide 15: Receiver behavior – Noise degradation
Noise/threshold degradation
N = KTBF
  KT: -174 dBm/Hz
  B: Receiver bandwidth (1/Pulse duration)
  F: Noise figure
I/N = I (dBm) – N (dBm)
Degradation > loss of sensitivity > loss of range
KT: -174 dBm/Hz
KTB: KT+ 10*log10(BW_Hz)
KTBF: KTB + NF
-6 dB
Safe
Chart: Threshold degradation calculations
Sensitivity = KTBF + SNR
Protection zone
Power (dBm)
Target
I
N
www.atdi.com
-174
-120
-117
-115

## Slide 16: Receiver behavior
Noise floor and detection threshold — set above receiver thermal noise to control false alarms CFAR (Constant False Alarm Rate) — threshold adapts locally to keep false-alarm probability constant in varying clutter MTI / MTD filters — suppress stationary returns by comparing successive pulses in the time or Doppler domain Doppler discrimination — moving targets pass the filter; stationary terrain and buildings are rejected Plot extractor and tracker — group detections into plots and tracks; have finite processing capacity
www.atdi.com
Notes: Now let’s look at how radar systems process what they receive.
Every radar has a noise floor, which comes from natural thermal noise in the receiver. To avoid false alarms, the detection threshold is set just above this level. Increasing noise-floor due to local reflections means reducing the sensitivity and risking early alarms.
To improve this further, radars use something called Constant False Alarm Rate, or CFAR. This means the detection threshold automatically adjusts depending on the local environment, helping maintain a consistent rate of false alarms even when clutter changes.
Radars also apply filtering techniques like MTI and MTD. These compare signals over time or frequency to suppress stationary objects—so things like terrain or buildings are filtered out.
This is where Doppler comes in. Moving targets, like aircraft, have a Doppler shift and can pass through these filters, while stationary objects are rejected.
Finally, the radar groups detections into plots and then into tracks. This tracking process has limited capacity, so too many false or clutter detections can impact overall performance.

## Slide 17: Radar antenna radiation pattern - relevance
Escape/re-entry point
Antenna discrimination in the direction of WT can be computed from vertical antenna pattern
www.atdi.com

## Slide 18: Radar antenna radiation patterns
Modern air-defense radars use phased-array antennas — a grid of radiating elements whose individual phases and amplitudes set the beam shape. The radiation pattern — main lobe width, sidelobe levels and gain — is determined by the number of elements, their spacing, amplitude tapering and element pattern. Key parameters drive the result: • Element count (Nx × Ny) — sets aperture and peak gain • Spacing (typically 0.5 λ) — avoids grating lobes • Amplitude taper — trades sidelobe level against beamwidth Patterns matter for this assessment: the vertical 3 dB beamwidth sets the shadowing clearance criterion, and the sidelobe level bounds off-axis reflection susceptibility.
Radar | Spacing (λ) | Vert. elements | Horiz. elements
FPS-117 | 0.5 | 44 | 32
TPS-77 | 0.5 | 34 | 32
TPS-78 | 0.5 | 22 | 48
GM200 | — | 30 | 40
www.atdi.com

## Slide 19: 2D: main beam, side lobes
www.atdi.com

## Slide 20: ATC Radars Vs modern radars
Single broad vertical beam – single collision domain Multi-beams (Pencil beams) – multi collision domain
Mitigation ready
www.atdi.com

## Slide 21: Propagation model
Free space loss
Visibility (FSL or nothing, K factor 1.33)
Area – sub-path attenuation
Lsp = 6.4 + 20 log₁₀[ν + √(1 + ν²)]
ν = √2 · (H / R)
www.atdi.com

## Slide 22: Bistatic geometry and self-interference
Bistatic radar — transmitter and receiver at different locations, linked by a common scattering target (the wind turbine)
The bistatic radar equation, expressed in logarithmic (dB) form as a link budget:
Self-interference — the radar's own transmission bounces off the turbine back to the same receiver, so R₁ = R₂ and Gt = Gr
The monostatic collapse doubles the path loss (2·FSL) — this is the dominant term driving the I/N calculation
www.atdi.com

## Slide 23: Wind Turbine RCS Prediction
Parameter | L-Band | S-Band
Reference measured RCS (dBsm), 113 m rotor | 40 | 48
Scaled RCS, 200 m rotor (dBsm) | 44.6 | 52.5
Scaled RCS, 200 m rotor (m²) | 28,916 | 176,367
www.atdi.com
Frequency, rotation and angle dependent
Higher frequency is higher RCS
Bigger size is bigger RCS

## Slide 24: Measured RCS
Industrial sized wind turbines and corresponding RCS measurements
Source:
www.atdi.com
2.3 MW
3.0 MW
1.8 MW
146.5 m
130 m
130-200 m

## Slide 25: Reflection and I/N degradation
Pt:16kW
G: 37 dBi
RCS
Disc
www.atdi.com

## Slide 26: Shadow zone and beam blockage
Shadow
A turbine in the radar line of sight attenuates the signal on both the outbound and return paths (considering terrain, earth curvature and K factor) The shadow extends behind the turbine as a wedge; angular width depends on turbine size vs wavelength PSR suffers two-way path attenuation — detection loss is compounded on both legs of the round trip SSR loses the interrogation or reply path — aircraft in the shadow may fail to respond Severity depends on turbine height, range from the radar, and the minimum target altitude that must be protected
Visibility
www.atdi.com

## Slide 27: Clearance analysis
www.atdi.com
Scanning angle
3dB: BW/2
Horizon
Clearance angle
The further away the WT the higher it can be before blocking
Clearance angle = scanning angle – Beamwidth / 2

## Slide 28: Doppler contamination from rotating blades
Rotating blades impart Doppler shifts to the reflected signal — the spectrum spreads across harmonics of the rotation rate Modern multi-megawatt turbines reach blade tip speeds of 50–80 m/s — well above typical MTI velocity thresholds Blade returns pass through the filter and appear as moving targets, generating false plots and tracks Affects PSR only — SSR does not use Doppler processing and is immune to this mechanism Mitigation via the I/N criterion — if the reflected return is below the noise floor, the spectrum is irrelevant
www.atdi.com
Notes: In a primary surveillance radar environment, rotating wind turbine blades introduce a unique challenge by imparting Doppler shifts to the reflected radar signal, effectively spreading the return across harmonics of the blade rotation rate. With modern multi-megawatt turbines reaching blade tip speeds in the range of 50 to 80 meters per second, these Doppler components often exceed typical moving target indicator thresholds. As a result, the radar system interprets these reflections as legitimate targets, leading to false plots and even persistent false tracks. It’s important to note that this effect is specific to primary surveillance radar, since secondary surveillance radar does not rely on Doppler processing and is therefore immune. One practical mitigation approach is based on the interference-to-noise criterion: if the reflected signal from the turbine remains below the radar’s noise floor, its spectral characteristics become inconsequential, effectively preventing it from impacting system performance.

## Slide 29: Doppler
750 Hz doppler is
  ~ 135 km/hr at 3 GHz
  ~ 405 km/hr at 1 GHz
For false target to take place
  Reflected signal >= threshold AND
  Rotational AND
  Line-of-sight
QinetiQ Proprietary
www.atdi.com

## Slide 30: Operational impact on air traffic surveillance
Detection degradation — raised CFAR threshold reduces probability of detecting genuine low-RCS targets False plots and tracks — blade Doppler returns and ghost echoes trigger spurious aircraft reports Tracking instability — swap, split or lost tracks on real aircraft in the affected range–azimuth cells Coverage gaps — shadow wedges create altitude bands where targets are not seen Controller workload — more plots to resolve, lower trust in the picture, safety case impacted
www.atdi.com
Notes: In operational terms, the presence of wind turbines can significantly degrade radar performance in several interconnected ways. First, detection capability is reduced because the CFAR threshold rises in response to increased clutter, which in turn lowers the probability of detecting genuine low-RCS targets. At the same time, Doppler returns from rotating blades, along with multipath or ghost echoes, can generate false plots and even sustained false tracks, cluttering the surveillance picture. This directly impacts tracking performance, where controllers may observe track swaps, splits, or even complete losses of real aircraft within affected range–azimuth cells. Additionally, physical shadowing from turbine structures can create coverage gaps—often appearing as wedge-shaped regions or altitude bands where targets are intermittently or completely undetected. All of this culminates in a higher controller workload: more ambiguous plots to interpret, reduced confidence in the radar picture, and ultimately implications for the overall safety case that must be carefully managed.

## Slide 31: Assessment approaches — screening vs detailed
Not every turbine needs a full engineering study — assessment is layered to focus effort where it matters Safeguarding — a small exclusion zone around the radar where no turbine is permitted Screening — geometric checks on range, line of sight and terrain to clear benign cases early Simple engineering assessment — tractable calculations for turbines in intermediate zones Detailed analysis — full I/N and beam-clearance simulation for turbines close in or in clear line of sight
EUROCONTROL GUID-0130
www.atdi.com

## Slide 32: NTIA TR-08-454 — sequential screening
Stage 1 — line of sight screening using a 4/3 effective earth radius model; cleared if beyond LOS Stage 2 — terrain shielding check including Fresnel zone clearance; cleared if adequately shielded Stage 3 — detailed engineering analysis of the two physical mechanisms: reflection and shadowing I/N acceptance thresholds — ultra-conservative ≤ −9 dB, conservative ≤ −6 dB
www.atdi.com

## Slide 33: Proposed work-flow
Fully automated using HTZ software
Batch visibility analysis
Batch I/N analysis
Batch clearance analysis
Final verdict
Mitigation measurements
www.atdi.com

## Slide 34: Single report with all computations
radar
WT

## Slide 35: Acceptance criteria — I/N and shadowing
Not within LOS? Accept
Two criteria must hold for a Conditional Accept — reflection (I/N) and shadowing (beam clearance) I/N ≤ −6 dB — reflected turbine return stays at least 6 dB below the receiver noise floor Covers all reflection effects — false targets, Doppler contamination and receiver overload all sit below detection Shadowing — elevation angle from radar to blade tip must be below the lower edge of the main beam Lower edge = scanning angle minus half the 3 dB vertical beamwidth, so blade tips sit under the main lobe
www.atdi.com

## Slide 36: Mitigation options for rejected turbines
Layout redesign — move or drop turbines to pull them out of the radar main beam or off the affected bearing Radar-absorbing cladding on tower and nacelle — reduces structural RCS and the I/N margin Stealth or radar-absorbing blade coatings — attenuates blade returns and limits Doppler contamination Fill-in radar — a supplementary sensor restores coverage inside the shadow wedge behind a wind farm Operational — PSR sector blanking, range-azimuth gating, antenna elevation adjustment where the operator accepts the trade-off
www.atdi.com

## Slide 37: Key takeaways and questions
Wind and radar can coexist — the engineering is well understood, and the assessment frameworks are mature Three mechanisms matter — reflection, shadowing, Doppler contamination Use a layered workflow — safeguarding, range and LOS screening before expensive detailed analysis Acceptance criteria — I/N ≤ −6 dB reflection and beam-clearance shadowing, worst-case across all radars
www.atdi.com

## Slide 38: Thank you Q/A
www.atdi.com
11 boulevard Malesherbes, 75008 Paris, FRANCE
ATDI Group
contact@atdi.com
+33 1 53 30 81 41

## Slide 39: HTZ Communications CNS Network Design & Optimisation
Dedicated aeronautical propagation models
Automated site network coverage, interference analysis and frequency planning
Identifying shadowing/black spots and automatic site search
Traffic analysis and network capacity management
Surveillance functions including multi-lateration (TDOA)
Ability to model ATC radars (VOR, ILS, MLAT, RADAR)
Functions to model wind turbine interference or
5G towers on aeronautical radars
ICAO building restriction compliance analysis and exclusion zones around the airports

## Slide 40: Visibility analysis
www.atdi.com

## Slide 41: I/N analysis
Full visibility, I/N and shadowing analysis
www.atdi.com

## Slide 42: Euro-control zones

## Slide 43: Propagation models

## Slide 44: Propagation losses